## Slide 1: Meeting-08
Magician project Update

## Slide 2: Completed Creating URDF for the Tool Assem
Creating the URDF model of the tool along with assigning the mass and the inertia to it.
Also the tool was equipped with the GPIO cable so that the tool can be controlled by the Doosan robot digital I/O pins

## Slide 3
Initial Design and the folded beam Structure

## Slide 4
Initial Analysis Results

## Slide 5
Design Optimization of the Folded beam Structure
Iyer, R. B., Jatti, V. K., Yadav, Y., Verma, A., Desai, J., & Dewan, C. P. (2017). Design optimization of CAD model. Materials Today: Proceedings, 4(8), 7357-7364.
constrained
constrained
L1
L2
L3
L4
B2
L5
B1
B4
B3
B5

## Slide 6
Initial Analysis Results
After Optimization
Here FOS is <1.5 ( Not suitable for Engineering Applications)

## Slide 7
Influential Design Parameters for Optimization
Design Goal: min(total_mass)
Design Limits : Modal frequency < 95 Hz
Variables: ( in mm)
1st Set  all the horizontal length ( 4 parameters)
10< L1 <20
30< L2 = L3 < 50
15 < L4 < 25
2nd Set  all the horizontal thickness (4 parameters)
1 < T <3
Where, T = T1 =T2 = T3 =T4
Observations:
Model frequencies are highly dependent on the horizontal beam dimensions .
2) No Variation during Vertical beam dimension changes.
3) From the prior Sensitivity Analysis we could found that the optimal width and height for the vertical beam structures those are
Overall folded beam Width : 5mm
Vertical beam Height:4 mm

## Slide 8
Modified Design and the folded beam Structure
Initial Design parameters
Single bent to double bent with added rounds

## Slide 9
Modified Design after Optimization

## Slide 10
Design Validation Calculations for the Modified Model
Mechanical Design Calculations (For Initial Version)
The current model is subjected to the tool weight of -25 N , gravitational load of 1g
also, a static load of -20 N in all the 3 axial directions
Maximum Stress – von Mises : 96.82MPa
Maximum Principal Strain : 0.00106
Maximum Strain Energy per Unit Volume : 0.06898 MPa
Factor or Safety ( Calculated) : 2.1223 ( Valid for most of Engineering Applications)
Ergal 70

## Slide 11
Results from Fatigue Analysis
Tested the Model Fatigue with a Desired Endurance of 210 cycles and verified as Safe until 1020 cycles ( Under loading conditions).
After the end of these cycles it’s shown that the modal will be highly effected in the Red Areas . At these spots the model could lead to breakage .

## Slide 13
FOS = 3.839

## Slide 14
FOS = 3.839
FOS = 3.869

## Slide 16
This stress analysis is actually under loading which is obtained from the ft sensor tests.
In the current analysis we have used the readings from a 0 orientation speed 3 settings in free condition loading ( under self weight)
Doosan Robot arm
tool

## Slide 17
This stress analysis is actually under loading which is obtained from the ft sensor tests.
In the current analysis we have used the readings from a 0 orientation speed 3 settings in free condition loading ( under self weight)
Doosan Robot arm
tool

## Slide 18
This stress analysis is actually under loading which is obtained from the ft sensor tests.
In the current analysis we have used the readings from a 0 orientation speed 3 settings in free condition loading ( under self weight)
Doosan Robot arm
tool

## Slide 21
For 4 mm thick beam widths

## Slide 22
For 6 mm thick beam widths

## Slide 25
Top_ holes
Bottom_ holes

## Slide 26
Top_ holes
Bottom_ holes

## Slide 36
FOS = 4.056

## Slide 37
Perform an modal analysis in Creo Simulate and obtain the initial Modal frequencies of the model
Design of CAD Model in Creo Parametric
Then Run the Sensitivity Analysis to evaluate which design parameters influence the Model’s Modal frequency
Perform the Design Optimization Analysis in Creo Simulate
Select the parameters which are need to be optimized
stop
Start
Specify the design parameter range which is within the design limit also specify the design limits that needs to be satisfied
Run the Optimization Study with the optimize goal being set
Specify the Optimization convergence and Maximum iterations.
does the result get converged?
Display the Optimized design results
If No
If Yes